## Slide 1: Project 6: Small Modular Reactors
William Gerding CJ Oldham Austin Stanford
Zack Taylor Patrick Williams

## Slide 2: Outline
Background
Properties
Methods
(Some) Results
Conclusion

## Slide 3: Background
Diffusion Approximation vs. Transport Theory
Why SMRs?
B&W mPower
NuScale NuScale
Our code
B&W mPower reactor assembly[1]
NuScale Reactor Assembly{2]
[1]http://www.modernpowersystems.com/features/featurenuscale-joins-bw-on-the-smr-bench-4264827/featurenuscale-joins-bw-on-the-smr-bench-4264827-2.html
[2]http://www.modernpowersystems.com/features/featurenuscale-joins-bw-on-the-smr-bench-4264827/featurenuscale-joins-bw-on-the-smr-bench-4264827-1.html

## Slide 4: Properties (mPower)
Shortened PWR fuel Assemblies (2.4 m vs. 4 m)
69 assemblies in core
Less than 5% Enrichment
More than 40 GWd/MT burnup
48 Month Cycle
530 MWth

## Slide 5: Properties (NuScale)
Shortened PWR fuel assemblies (2 m vs. 4 m)
37 Fuel Assemblies
Less than 4.95% Enrichment
Burnup is not yet determined
24 Month Cycle
160 MWth

## Slide 6: Methods
Used a SCALE simulation based on previous properties to determine input cross sections
Python was used for determining flux
  Selected for flexibility and speed
Flux was normalized based on reactor power
Cases were ran for both reactor types with their respective cross sections

## Slide 7: Methods (SCALE)
For obtaining the cross-sections we made a SCALE model based off the 17x17 PWR array. Both SMRs use the same bundles as you would find in a PWR. The only major difference is the height of the core.
We ran two different steady state and
depletion models for the reactor design.
  NuScale Reactor
  Mpower Reactor
Cross-Section for 17x17 bundle.

## Slide 8: Methods (SCALE)
mPower Reactor
4.95 % Enrichment
  Close to the 5% enrichment we saw online.
530 MWth
Burnup
  0, 15, 30, 45 GWD/MTHIM
NuScale Reactor
3.1% Enrichment
  Also ran it with 4.05, 4.55, and 2.6% enrichment.
160 MWth
Burnup
  0, 15, 30, 45 GWD/MTHIM

## Slide 9: Methods (SCALE)
The basic core loading pattern for the NuScale reactor with 37 total bundles spread across the core.
Cutout of the SCALE file showing ¼ of the 17x17 fuel bundle.

## Slide 10: Scale Results
Results showing the cross sections obtained by the two depletion models.
mPower Cross Sections |  |  |  |  |  |  | 
Burnup (GWd/MT) | Group | Total | Transport | Removal | Eff Abs | Nu-Fission | Scatter Down
0 | 1 | 5.32E-01 | 2.26E-01 | 2.53E-02 | 9.94E-03 | 8.73E-03 | 1.55E-02
 | 2 | 1.38E+00 | 8.89E-01 | 1.11E-01 | 1.10E-01 | 1.98E-01 | 1.71E-03
15 | 1 | 5.39E-01 | 2.28E-01 | 2.63E-02 | 1.07E-02 | 7.46E-03 | 1.56E-02
 | 2 | 1.40E+00 | 9.09E-01 | 1.21E-01 | 1.19E-02 | 1.86E-01 | 1.82E-03
30 | 1 | 5.44E-01 | 2.29E-01 | 2.69E-02 | 1.12E-02 | 6.41E-03 | 1.56E-02
 | 2 | 1.40E+00 | 9.19E-01 | 1.17E-01 | 1.15E-01 | 1.69E-01 | 1.75E-03
45 | 1 | 5.48E-01 | 2.31E-01 | 2.74E-02 | 1.17E-02 | 5.50E-03 | 1.57E-02
 | 2 | 1.40E+00 | 9.23E-01 | 1.09E-01 | 1.08E-01 | 1.46E-01 | 1.63E-03
NuScale Cross Sections |  |  |  |  |  |  | 
Burnup (GWd/MT) | Group | Total | Transport | Removal | Eff Abs | Nu-Fission | Scatter Down
0 | 1 | 5.35E-01 | 2.27E-01 | 2.61E-02 | 1.05E-02 | 8.80E-03 | 1.56E-02
 | 2 | 1.37E+00 | 8.81E-01 | 1.22E-01 | 1.20E-01 | 1.93E-01 | 2.22E-03
15 | 1 | 5.43E-01 | 2.29E-01 | 2.65E-02 | 9.95E-03 | 5.50E-03 | 1.66E-02
 | 2 | 1.38E+00 | 9.08E-01 | 9.27E-02 | 9.13E-02 | 1.32E-01 | 1.43E-03
30 | 1 | 5.48E-01 | 2.31E-01 | 2.72E-02 | 1.07E-02 | 4.73E-03 | 1.65E-02
 | 2 | 1.39E+00 | 9.17E-01 | 8.97E-02 | 8.82E-02 | 1.17E-01 | 1.37E-03
45 | 1 | 5.52E+00 | 2.32E-01 | 2.78E-02 | 1.13E-02 | 4.19E-03 | 1.65E-02
 | 2 | 1.38E+00 | 9.20E-01 | 8.49E-02 | 8.36E-02 | 1.01E-01 | 1.28E-03

## Slide 11: Results
Thermal
Fast
Keff = 1.0025367
Z = 2000cm
Dfuel = 18cm
Dwater = 15cm
5 Mesh per Element
10 Mesh per ln(z)
Loading Pattern = [Fuel B, Fuel A, Fuel B, Fuel C, Water

## Slide 12: Results (Mostly Burnt)
Thermal
Fast
Keff = .967264
Z = 2000cm
Dfuel = 18cm
Dwater = 15cm
5 Mesh per Element
10 Mesh per ln(z)
Loading Pattern = [Fuel B, Fuel B, Fuel B, Fuel B, Water

## Slide 13: Conclusion
Reactor simulations are essential
  Cost, time, etc
Too complex for one software
  Many codes must be used interdependently
Many assumptions to simplify
  Steady-state, just the core